# Getting Started

## 1.1	PACKAGE CONTENTS

ACD-3100				            Warranty Card

Product CD				            Terminal Blocks & Screws

Power Adaptor (Option)

## 1.2 PHYSICAL DESCRIPTION

Read the following information to familiarize yourself with the video Decoder, and make particular notes of where the connectors and LEDs are located.

- Action LED Indicator

The LED will light up after IP device has successfully completed the boot process.

- Serial Port LED Indicator

LEDs indicating when serial port is active.

- Reset Button

Step 1: Switch off IP device by disconnecting the power cable

Step 2: Using a suitable pointed object, press and continue to hold the Reset Button depressed. While continuing to hold the reset button depressed, reconnect the power cable.

Step 3: Keep holding the reset button depressed around 6 seconds, release the reset button. The unit will start up with factory default settings.

- Terminal Blocks Pin 1~6

The IP device supports two alarm input and two alarm output.  DI: Logic Level 0: 0~0.4V; Logic Level 1: 3.3~30V         DO: Logic Level 0: 0.1~0.6V; Logic Level1: 2.4~5V

Please find Support package” TS-00045” for details.

| PIN | NAME | DESCRIPTION |
| --- | --- | --- |
| 1 | DO1 | Digital Output 1 |
| 2 | DO2 | Digital Output 2 |
| 3 | GND | Ground Pin |
| 4 | DI1 | Digital Input 1 |
| 5 | DI2 | Digital Input 2 |
| 6 | GND | Ground Pin |

- Terminal Blocks Pin 7~12
Pin 7~10: RS232/422/485. Default mode is RS-485

Pin 11~12: DC 12V power input

| PIN | NAME | DESCRIPTION |
| --- | --- | --- |
|  |  | RS-485 | RS-422 | RS-232 |
| 7 | Tx+ | D+ | Tx+ | Tx |
| 8 | Tx- | D- | Tx- |  |
| 9 | Rx+ |  | Rx+ | Rx |
| 10 | Rx- |  | Rx- |  |
| 11 | 12V | Power Input (DC +12V) |
| 12 | GND | Ground Pin of Power Input & RS-232 |

- Ethernet Port
The IP device connects to the Ethernet via a standard RJ45 connector. Supporting NWAY, this IP device can auto detect the speed of local network segment (10Base-T/100Base-TX Ethernet).

- Dip Switch for Serial Port
RS-485 or RS-422 pin define (default is RS-485)

RS-232 pin define

- Audio Input / Output

The IP device supports one audio input and output with earphone jack

- Y/C Output

Analog Video Output of Y/C Signal with S-Video Connector

- Composite Output

Analog Video Output of Composite Signal with BNC Connector

## 1.3 CONNECT NECESSARY CABLES

Follow the procedures below to connect the video Decoder to the respective apparatuses.

- The IP camera or other encoding devices as a video source

- The video server or other encoding devices as a video source

- Connect video server / IP camera and video Decoder to an Ethernet hub (RJ45 connectors)

- Video Decoder is the receiver side

- Connect a coaxial cable to TV monitor and display the video which encoded and transferred from video server / IP camera

# Quick Tour

This section guides you with a quick tour on our video Decoder.

## 2.1 Configure the video Decoder

2.1.1 Make sure network environment

Default IP of video Decoder is 192.168.0.200. Please make sure the video Decoder and your PC are on the same network segment before running the installation.

    - Open Internet Explorer with IP address

This section describes how to configure the video Decoder. The product administrator has unlimited access to all setup windows and normal users can only watch the live images. The video Decoder is configured under a standard browser (Microsoft Internet Explorer 6.0 or above).

Follow the procedures below to configure the video Decoder.

- STEP1: Open a browser

- STEP2: Enter the IP address of the video Decoder.

The default IP address is “192.168.0.200”

- STEP3: Enter the Account name (factory default: Admin) and the Password (factory default: 123456).

- STEP4: Select the language of the video Decoder user interface. You can select from English, Traditional Chinese, Simplified Chinese, Japanese and Spanish.

- STEP5: Click the  button to login or click the button to re-enter again.

    - Set a new IP address

*IP Address : The IP address of the LAN interface. The default IP address is 192.168.0.200.

*Subnet Mask : The subnet mask of the LAN interface.The default subnet mask is 255.255.255.0

*Click  button

    - Select a video server / IP camera

This section tells you how to setup video server or IP camera’s video and streaming settings.

*Source Type : Select your video source is Video Server or Quad Server.

*Connect Type : Select Multicast or TCP mode for connecting to a video server/IP camera.

*Variable FPS : Select variable FPS.

*TCP Connect IP : Set IP address of a video server / IP camera while Connect Type is TCP Streaming.

*Multicast Connect IP: Set IP address of video server / IP camera while Connect Type is Multicast streaming.

*Connect User Name : Set Login Name of video server / IP camera.

*Connect Password : Set Password of video server / IP camera.

*Click  button

|  | NOTE: Check with your MIS department, if video Decoder and video server/IP camera are setting in different VLANs, please connect to WAN port. |
| --- | --- |

    - Click Save Reboot to restore all settings and please wait about 30 seconds for system reboot.

# Text boxes

Video Decoder

ACD-3100

Ver. 070713

Quick Installation Guide

Please set the settings as below.

IP address: 192.168. 0.xxx

Subnet mask: 255.255.255.  0

(NOTE: xxx should be a number from 1 to 254, but 200 is excepted.)