# Getting Started

## 1.1		PACKAGE CONTENTS

ACM-3401/3411		        Power Adaptor (Option)

Product CD  			        Accessory

Warranty Card				  	Drill Template

## 1.2		PHYSICAL DESCRIPTION

- Reset Button

Step 1: Switch off IP device by disconnecting the power cable

Step 2: Press and continue to hold the Reset Button. Reconnect the power cable while continuing to hold the reset button.

Step 3: Keep holding the reset button depressed for a while, release the reset button. The unit will start up with factory default settings.

- Ethernet Port

The IP device connects to the Ethernet via a standard RJ45 connector. Supporting NWAY, this IP device can auto detect the speed of local network segment (10Base-T/100Base-TX Ethernet).

- Power Input
If your power input is DC12V. Please follow the description on the connector to connect to power.

| PIN | NAME | DESCRIPTION |
| --- | --- | --- |
| 1 | 12V | DC Power Input |
| 2 | GND | Ground Pin |

- Audio Input / Output

The IP device supports audio input and output with terminal block.

## 1.3 	BASIC CONNECTIONS

Follow the procedures below to connect the IP device to the respective apparatuses.

- Connect the power adaptor to IP device

- Connect IP device’s ethernet port to an Ethernet (RJ45 connectors). If your IP device has PoE built-in, you can regard it as a PD and connect it directly to a PSE device like PoE switch.

- Connect a PC to the Ethernet hub (RJ45 connectors)

|  | NOTE: You may find a support package for help you getting familiar with PoE. Please visit our web site, and get the support document TS-00040. |
| --- | --- |

1

# Quick Tour

This section guides you with a quick tour on this IP device.

2.1 Configure this IP Device

2.1.1	Make sure network environment

Default IP of this IP device is 192.168.0.100. Please make sure this IP device and your PC are on the same network segment before running the installation.

    - Open Internal Explorer with IP address

|  | NOTE: If your web browser is earlier than IE6, then download IE6 is recommended. |
| --- | --- |
|  | NOTE: This IP device default IP address is set to 192.168.0.100 |

    - Login with default administrator’s account & password

|  | NOTE: Default administrator account is set to Admin, password is set to 123456, and click button. |
| --- | --- |

    - Preview the video

    - Set the new IP address

*IP Address : The default IP address is 192.168.0.100.

*Subnet Mask : The default subnet mask is 255.255.255.0

*Click  button

|  | NOTE: In your Client PC, please make sure the setting of Network Connections Type is set to Auto Negotation, since this IP device follows MII standard. Otherwise, you might not see the live image. |
| --- | --- |
|  | IMPORTANT: After the IP address is changed, please record this IP address. There’s no way to connect to the IP device if user forgets the new IP address. |

    - Check Default Video Setting

    - Click Save Reboot to restore all settings and please wait about 30 seconds for system reboot.

# Text boxes

1

Megapixel IP Dome

ACM-3401

Megapixel Day&Night IP Dome

ACM-3411

Ver. 080130

Quick Installation Guide

2

Please set the settings as below.

IP address: 192.168. 0.xxx

Subnet mask: 255.255.255.  0

(NOTE: xxx should be a number from 1 to 254, but 100 is excepted.)