# Getting Started

## 1.1		PACKAGE CONTENTS

ACM-7411 series		      Power Adaptor (Option)

(DC12V / PoE )

Product CD  			      Terminal Blocks for Power, DI/O & Audio

Warranty Card				  Accessory

## 1.2		PHYSICAL DESCRIPTION

- Ethernet Port

The IP device connects to the Ethernet via a standard RJ45 connector. Supporting NWAY, this IP device can auto detect the speed of local network segment (10Base-T/100Base-TX Ethernet).

- Power Input
If your power input is DC12V. Please follow the description on the connector to connect to power.

| PIN | NAME | DESCRIPTION |
| --- | --- | --- |
| 1 | 12V | DC Power Input |
| 2 | GND | Ground Pin |

- Power Input Audio & DIO input/output

| PIN | NAME | DESCRIPTION |
| --- | --- | --- |
| 1 | DIO PW | DC12VIN |
| 2 | DIO GND | DGND |
| 3 | DO | DO1_TO_OUTSIDE |
| 4 | DI | DI1_FROM_OUTSIDE |
| 5 | AO_GND | DGND |
| 6 | A_OUT | Audio_OUT_LR |
| 7 | AI_GND | DGND |
| 8 | A_IN | Audio_IN |

- Reset Button

Step 1: Switch off IP device by disconnecting the power cable

Step 2: Press and continue to hold the Reset Button. Reconnect the power cable while continuing to hold the reset button.

Step 3: Keep holding the reset button depressed around 6 seconds, release the reset button. The unit will start up with factory default settings.

- Conduit Hole

These conduit holes are used for cables to go through.

## 1.3 	INSTALLATION PROCEDURE

There are three types of installation of this IP outdoor rugged dome series.

|  | Surface mount | Flush mount | Wall mount |
| --- | --- | --- | --- |
| Pictures |  |  |  |
| Optional Bracket required |  | ● | ● |

The mounting procedure can be divided into two parts,

1st: Connect the IP outdoor rugged dome series

2nd: Mount the IP outdoor rugged dome series

## Connect the IP Outdoor Rugged Dome

### 1.3.1.1	Remove the cover

Remove the dome cover with special hex wrench in the accessory bag.

### 1.3.1.2	Insert the cabl

There are two conduit holes, one is at the dome bottom and the other one is at the side of rugged dome with plug. Remove the plug if your cable will go through the one at the side of rugged dome

### 1.3.1.3	Connect cables to connectors

Please follow the instruction at Chapter 2: Physical Description, for how to connect to each connector.

## Mount the IP Outdoor Fixed Dome (Surface)

## Mount the IP Outdoor Fixed Dome (Flush)

## Mount the IP Indoor Fixed Dome (Wall)

# Quick Tour

This section guides you with a quick tour on this IP device.

2.1 Configure this IP Device

2.1.1	Make sure network environment

Default IP of this IP device is 192.168.0.100. Please make sure this IP device and your PC are on the same network segment before running the installation.

    - Open Internal Explorer with IP address

|  | NOTE: If your web browser is earlier than IE6, then download IE6 is recommended. |
| --- | --- |
|  | NOTE: This IP device default IP address is set to 192.168.0.100 |

    - Login with default administrator’s account & password

|  | NOTE: Default administrator account is set to Admin, password is set to 123456, and click button. |
| --- | --- |

    - Preview the video

    - Set the new IP address

*IP Address : The default IP address is 192.168.0.100.

*Subnet Mask : The default subnet mask is 255.255.255.0

*Click  button

|  | NOTE: In your Client PC, please make sure the setting of Network Connections Type is set to Auto Negotation, since this IP device follows MII standard. Otherwise, you might not see the live image. |
| --- | --- |
|  | IMPORTANT: After the IP address is changed, please record this IP address. There’s no way to connect to the IP device if user forgets the new IP address. |

    - Check Default Video Setting

    - Click Save Reboot to restore all settings and please wait about 30 seconds for system reboot.

# Text boxes

1

MegaPixel IP Outdoor Rugged Dome

(with DC 12V / PoE)

ACM-7411 series

Ver. 080410

Quick Installation Guide

2

Please set the settings as below.

IP address: 192.168. 0.xxx

Subnet mask: 255.255.255.  0

(NOTE: xxx should be a number from 1 to 254, but 100 is excepted.)